Function generator

Date: Jun 2024

# RTL
## Description
Function generator module. The module has a selector to choose between the following four functions:
- Sine
- Cosine
- Triangular
- Square
1. It is possible to set the output signal amplitude with a integer range from 1 to 7. When amplitude is change, the funtion is reset. When the amplitude takes negative values , it allows the output signal to be inverted.
2. To modify the amplitude, the configuration enable must be set to 1. During the period that enh_conf_i is set, no signal will be generated and wr_en_o will be disabled.
3. The function period is 256 clock cycles. Considering a clock frequency of 100MHz (Period = 10ns), each period of the generated function would be 2.56us and its frequency would be approximately 390.6 Khz.
4. When the reset is activated all the initial signals in position 0 which for each signal is as follows:
- Sine = 0
- Cosine = Amplitude
- Square = Amplitude
- Triangular = 0
When the enable is activated the signal at the output will continue at the point where it stopped previously, if a different function is selected, the new waveform will continue in the direction of the LUT where the previous function stopped since all four functions will use the same direction.

Table 1: Inputs/Outputs description

Input	Size	Description	Source
clk	1	Clock	Clock source
rst	1	Asynchronous reset activated	Main input
en_low_i	1	Operation enable. This enable activates the operation of the module when it is set to zero. When en_low_i = 1, the module stops its operation at the point where it was and all signals retain their value until the enable is re-asserted.	Main input / (full / FIFO)
enh_conf_i	1	Configuration enable. This signal enables the amplitud change.	Main inout
amp_i	4	Amplitude of the function. It can take the integer values -7, -6, -5, -4, -3, -2, -1, 1, 2, 3, 4, 5, 6 and 7 in a 2’s complement format. It determines the amplitude of the output signal. Binary values 0000 and 1000 are forbiden, whwn the input takes these values and enh_config_i=1, the amplitud will not be modified.	Main input
sel_i	2	Function selector Allows to select which waveform is the one we want to obtain in the output of the module. The function of each value of this signal is described in a table below.	Main input

Output	Size	Description	Source
data_o	32	Data of the generated function	Top module
wr_en_o	1	This signal indicates that the data at the output are valid and will be written to a destination memory.	Top module

Internal sub-modules:
- Adder module
- Multiplication module
- Register module
- LUT
- FSM module
- Mux module
## Sub-modules

Adder: 3-input adder with enable and clear. The addition is performed combinationally when the enable is active. The output is zero when the clear is activated. The clear signal has priority.

1. Multiplier: 2-input multiplier with enable. Multiplication is performed combinationally when the enable is active.
2. Register: Type D flip flop register activated on positive clock edge with enable active high and clear active high
3. FSM: The state machine will control the enable of the internal modules, when to clear the information from the registers and the sequential operation of the whole RTL.

(Diagrama temporal- falta descripcion de los estados)

Mux: 4-input 1-output multiplexer with a 2-bit selector switch. The output signal corresponds to the selector value (0 to 3). Inputs and outputs are signed.

sel_i value	Output signal
0	Sine
1	Cosine
2	Triangular
3	Square

LUT: Stores the values of the functions. It only has the operation of reading by means of an address. Its content is loaded by means of a txt file in hexadecimal. The reading is sequential on the positive edge of the clock. Information on each function can be found in the annexes section.

# Verification
## Formal

N#	Name	Description	Code
Assumptions
1
Covers
1
2
1

Table 2: Properties description
## Results

# Anexos:
## LUT data

LUT	Square			Triangular
	Dec	Bin	Hex	Dec	Bin	Hex
0 / 1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34 / 35 / 36 / 37 / 38 / 39 / 40 / 41 / 42 / 43 / 44 / 45 / 46 / 47 / 48 / 49 / 50 / 51 / 52 / 53 / 54 / 55 / 56 / 57 / 58 / 59 / 60 / 61 / 62 / 63 / 64 / 65 / 66 / 67 / 68 / 69 / 70 / 71 / 72 / 73 / 74 / 75 / 76 / 77 / 78 / 79 / 80 / 81 / 82 / 83 / 84 / 85 / 86 / 87 / 88 / 89 / 90 / 91 / 92 / 93 / 94 / 95 / 96 / 97 / 98 / 99 / 100 / 101 / 102 / 103 / 104 / 105 / 106 / 107 / 108 / 109 / 110 / 111 / 112 / 113 / 114 / 115 / 116 / 117 / 118 / 119 / 120 / 121 / 122 / 123 / 124 / 125 / 126 / 127 / 128 / 129 / 130 / 131 / 132 / 133 / 134 / 135 / 136 / 137 / 138 / 139 / 140 / 141 / 142 / 143 / 144 / 145 / 146 / 147 / 148 / 149 / 150 / 151 / 152 / 153 / 154 / 155 / 156 / 157 / 158 / 159 / 160 / 161 / 162 / 163 / 164 / 165 / 166 / 167 / 168 / 169 / 170 / 171 / 172 / 173 / 174 / 175 / 176 / 177 / 178 / 179 / 180 / 181 / 182 / 183 / 184 / 185 / 186 / 187 / 188 / 189 / 190 / 191 / 192 / 193 / 194 / 195 / 196 / 197 / 198 / 199 / 200 / 201 / 202 / 203 / 204 / 205 / 206 / 207 / 208 / 209 / 210 / 211 / 212 / 213 / 214 / 215 / 216 / 217 / 218 / 219 / 220 / 221 / 222 / 223 / 224 / 225 / 226 / 227 / 228 / 229 / 230 / 231 / 232 / 233 / 234 / 235 / 236 / 237 / 238 / 239 / 240 / 241 / 242 / 243 / 244 / 245 / 246 / 247 / 248 / 249 / 250 / 251 / 252 / 253 / 254 / 255	1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / 1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000 / -1.0000	0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 0001 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000 / 1111 0000000000000000000000000000	10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / 10000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000 / F0000000	0.0000 / 0.0156 / 0.0312 / 0.0469 / 0.0625 / 0.0781 / 0.0938 / 0.1094 / 0.1250 / 0.1406 / 0.1562 / 0.1719 / 0.1875 / 0.2031 / 0.2188 / 0.2344 / 0.2500 / 0.2656 / 0.2812 / 0.2969 / 0.3125 / 0.3281 / 0.3438 / 0.3594 / 0.3750 / 0.3906 / 0.4062 / 0.4219 / 0.4375 / 0.4531 / 0.4688 / 0.4844 / 0.5000 / 0.5156 / 0.5312 / 0.5469 / 0.5625 / 0.5781 / 0.5938 / 0.6094 / 0.6250 / 0.6406 / 0.6562 / 0.6719 / 0.6875 / 0.7031 / 0.7188 / 0.7344 / 0.7500 / 0.7656 / 0.7812 / 0.7969 / 0.8125 / 0.8281 / 0.8438 / 0.8594 / 0.8750 / 0.8906 / 0.9062 / 0.9219 / 0.9375 / 0.9531 / 0.9688 / 0.9844 / 1.0000 / 0.9844 / 0.9688 / 0.9531 / 0.9375 / 0.9219 / 0.9062 / 0.8906 / 0.8750 / 0.8594 / 0.8438 / 0.8281 / 0.8125 / 0.7969 / 0.7812 / 0.7656 / 0.7500 / 0.7344 / 0.7188 / 0.7031 / 0.6875 / 0.6719 / 0.6562 / 0.6406 / 0.6250 / 0.6094 / 0.5938 / 0.5781 / 0.5625 / 0.5469 / 0.5312 / 0.5156 / 0.5000 / 0.4844 / 0.4688 / 0.4531 / 0.4375 / 0.4219 / 0.4062 / 0.3906 / 0.3750 / 0.3594 / 0.3438 / 0.3281 / 0.3125 / 0.2969 / 0.2812 / 0.2656 / 0.2500 / 0.2344 / 0.2188 / 0.2031 / 0.1875 / 0.1719 / 0.1562 / 0.1406 / 0.1250 / 0.1094 / 0.0938 / 0.0781 / 0.0625 / 0.0469 / 0.0312 / 0.0156 / 0.0000 / -0.0156 / -0.0312 / -0.0469 / -0.0625 / -0.0781 / -0.0938 / -0.1094 / -0.1250 / -0.1406 / -0.1562 / -0.1719 / -0.1875 / -0.2031 / -0.2188 / -0.2344 / -0.2500 / -0.2656 / -0.2812 / -0.2969 / -0.3125 / -0.3281 / -0.3438 / -0.3594 / -0.3750 / -0.3906 / -0.4062 / -0.4219 / -0.4375 / -0.4531 / -0.4688 / -0.4844 / -0.5000 / -0.5156 / -0.5312 / -0.5469 / -0.5625 / -0.5781 / -0.5938 / -0.6094 / -0.6250 / -0.6406 / -0.6562 / -0.6719 / -0.6875 / -0.7031 / -0.7188 / -0.7344 / -0.7500 / -0.7656 / -0.7812 / -0.7969 / -0.8125 / -0.8281 / -0.8438 / -0.8594 / -0.8750 / -0.8906 / -0.9062 / -0.9219 / -0.9375 / -0.9531 / -0.9688 / -0.9844 / -1.0000 / -0.9844 / -0.9688 / -0.9531 / -0.9375 / -0.9219 / -0.9062 / -0.8906 / -0.8750 / -0.8594 / -0.8438 / -0.8281 / -0.8125 / -0.7969 / -0.7812 / -0.7656 / -0.7500 / -0.7344 / -0.7188 / -0.7031 / -0.6875 / -0.6719 / -0.6562 / -0.6406 / -0.6250 / -0.6094 / -0.5938 / -0.5781 / -0.5625 / -0.5469 / -0.5312 / -0.5156 / -0.5000 / -0.4844 / -0.4688 / -0.4531 / -0.4375 / -0.4219 / -0.4062 / -0.3906 / -0.3750 / -0.3594 / -0.3438 / -0.3281 / -0.3125 / -0.2969 / -0.2812 / -0.2656 / -0.2500 / -0.2344 / -0.2188 / -0.2031 / -0.1875 / -0.1719 / -0.1562 / -0.1406 / -0.1250 / -0.1094 / -0.0938 / -0.0781 / -0.0625 / -0.0469 / -0.0312 / -0.0156	0000 0000000000000000000000000000 / 0000 0000001111111110010111001001 / 0000 0000011111111100101110010010 / 0000 0000110000000001101000110110 / 0000 0001000000000000000000000000 / 0000 0001001111111110010111001001 / 0000 0001100000000011010001101101 / 0000 0001110000000001101000110110 / 0000 0010000000000000000000000000 / 0000 0010001111111110010111001001 / 0000 0010011111111100101110010010 / 0000 0010110000000001101000110110 / 0000 0011000000000000000000000000 / 0000 0011001111111110010111001001 / 0000 0011100000000011010001101101 / 0000 0011110000000001101000110110 / 0000 0100000000000000000000000000 / 0000 0100001111111110010111001001 / 0000 0100011111111100101110010010 / 0000 0100110000000001101000110110 / 0000 0101000000000000000000000000 / 0000 0101001111111110010111001001 / 0000 0101100000000011010001101101 / 0000 0101110000000001101000110110 / 0000 0110000000000000000000000000 / 0000 0110001111111110010111001001 / 0000 0110011111111100101110010010 / 0000 0110110000000001101000110110 / 0000 0111000000000000000000000000 / 0000 0111001111111110010111001001 / 0000 0111100000000011010001101101 / 0000 0111110000000001101000110110 / 0000 1000000000000000000000000000 / 0000 1000001111111110010111001001 / 0000 1000011111111100101110010010 / 0000 1000110000000001101000110110 / 0000 1001000000000000000000000000 / 0000 1001001111111110010111001001 / 0000 1001100000000011010001101101 / 0000 1001110000000001101000110110 / 0000 1010000000000000000000000000 / 0000 1010001111111110010111001001 / 0000 1010011111111100101110010010 / 0000 1010110000000001101000110110 / 0000 1011000000000000000000000000 / 0000 1011001111111110010111001001 / 0000 1011100000000011010001101101 / 0000 1011110000000001101000110110 / 0000 1100000000000000000000000000 / 0000 1100001111111110010111001001 / 0000 1100011111111100101110010010 / 0000 1100110000000001101000110110 / 0000 1101000000000000000000000000 / 0000 1101001111111110010111001001 / 0000 1101100000000011010001101101 / 0000 1101110000000001101000110110 / 0000 1110000000000000000000000000 / 0000 1110001111111110010111001001 / 0000 1110011111111100101110010010 / 0000 1110110000000001101000110110 / 0000 1111000000000000000000000000 / 0000 1111001111111110010111001001 / 0000 1111100000000011010001101101 / 0000 1111110000000001101000110110 / 0001 0000000000000000000000000000 / 0000 1111110000000001101000110110 / 0000 1111100000000011010001101101 / 0000 1111001111111110010111001001 / 0000 1111000000000000000000000000 / 0000 1110110000000001101000110110 / 0000 1110011111111100101110010010 / 0000 1110001111111110010111001001 / 0000 1110000000000000000000000000 / 0000 1101110000000001101000110110 / 0000 1101100000000011010001101101 / 0000 1101001111111110010111001001 / 0000 1101000000000000000000000000 / 0000 1100110000000001101000110110 / 0000 1100011111111100101110010010 / 0000 1100001111111110010111001001 / 0000 1100000000000000000000000000 / 0000 1011110000000001101000110110 / 0000 1011100000000011010001101101 / 0000 1011001111111110010111001001 / 0000 1011000000000000000000000000 / 0000 1010110000000001101000110110 / 0000 1010011111111100101110010010 / 0000 1010001111111110010111001001 / 0000 1010000000000000000000000000 / 0000 1001110000000001101000110110 / 0000 1001100000000011010001101101 / 0000 1001001111111110010111001001 / 0000 1001000000000000000000000000 / 0000 1000110000000001101000110110 / 0000 1000011111111100101110010010 / 0000 1000001111111110010111001001 / 0000 1000000000000000000000000000 / 0000 0111110000000001101000110110 / 0000 0111100000000011010001101101 / 0000 0111001111111110010111001001 / 0000 0111000000000000000000000000 / 0000 0110110000000001101000110110 / 0000 0110011111111100101110010010 / 0000 0110001111111110010111001001 / 0000 0110000000000000000000000000 / 0000 0101110000000001101000110110 / 0000 0101100000000011010001101101 / 0000 0101001111111110010111001001 / 0000 0101000000000000000000000000 / 0000 0100110000000001101000110110 / 0000 0100011111111100101110010010 / 0000 0100001111111110010111001001 / 0000 0100000000000000000000000000 / 0000 0011110000000001101000110110 / 0000 0011100000000011010001101101 / 0000 0011001111111110010111001001 / 0000 0011000000000000000000000000 / 0000 0010110000000001101000110110 / 0000 0010011111111100101110010010 / 0000 0010001111111110010111001001 / 0000 0010000000000000000000000000 / 0000 0001110000000001101000110110 / 0000 0001100000000011010001101101 / 0000 0001001111111110010111001001 / 0000 0001000000000000000000000000 / 0000 0000110000000001101000110110 / 0000 0000011111111100101110010010 / 0000 0000001111111110010111001001 / 0000 0000000000000000000000000000 / 1111 1111110000000001101000110111 / 1111 1111100000000011010001101110 / 1111 1111001111111110010111001010 / 1111 1111000000000000000000000000 / 1111 1110110000000001101000110111 / 1111 1110011111111100101110010101 / 1111 1110001111111110010111001010 / 1111 1110000000000000000000000000 / 1111 1101110000000001101000110111 / 1111 1101100000000011010001101110 / 1111 1101001111111110010111001010 / 1111 1101000000000000000000000000 / 1111 1100110000000001101000110111 / 1111 1100011111111100101110010011 / 1111 1100001111111110010111001010 / 1111 1100000000000000000000000000 / 1111 1011110000000001101000110111 / 1111 1011100000000011010001101110 / 1111 1011001111111110010111001010 / 1111 1011000000000000000000000000 / 1111 1010110000000001101000110111 / 1111 1010011110111100101110010011 / 1111 1010001111111110010111001010 / 1111 1010000000000000000000000000 / 1111 1001110000000001101000110111 / 1111 1001100000000011010001101110 / 1111 1001001111111110010111001010 / 1111 1001000000000000000000000000 / 1111 1000110000000001101000110111 / 1111 1000011111111100101110010011 / 1111 1000001111111110010111001010 / 1111 1000000000000000000000000000 / 1111 0111110000000001101000110111 / 1111 0111100000000011010001101110 / 1111 0111001111111110010111001010 / 1111 0111000000000000000000000000 / 1111 0110110000000001101000110111 / 1111 0110011111111100101110010011 / 1111 0110001111111110010111001010 / 1111 0110000000000000000000000000 / 1111 0101110000000001101000110111 / 1111 0101100000000011010001101110 / 1111 0101001111111110010111001010 / 1111 0101000000000000000000000000 / 1111 0100110000000001101000110111 / 1111 0100011111111100101110010011 / 1111 0100001111111110010111001010 / 1111 0100000000000000000000000000 / 1111 0011110000000001101000110111 / 1111 0011100000000011010001101110 / 1111 0011001111111110010111001010 / 1111 0011000000000000000000000000 / 1111 0010110000000001101000110111 / 1111 0010011111111100101110010011 / 1111 0010001111111110010111001010 / 1111 0010000000000000000000000000 / 1111 0001110000000001101000110111 / 1111 0001100000000011010001101110 / 1111 0001001111111110010111001010 / 1111 0001000000000000000000000000 / 1111 0000110000000001101000110111 / 1111 0000011111111100101110010011 / 1111 0000001111111110010111001010 / 1111 0000000000000000000000000000 / 1111 0000001111111110010111001010 / 1111 0000011111111100101110010011 / 1111 0000110000000001101000110111 / 1111 0001000000000000000000000000 / 1111 0001001111111110010111001010 / 1111 0001100000000011010001101110 / 1111 0001110000000001101000110111 / 1111 0010000000000000000000000000 / 1111 0010001111111110010111001010 / 1111 0010011111111100101110010011 / 1111 0010110000000001101000110111 / 1111 0011000000000000000000000000 / 1111 0011001111111110010111001010 / 1111 0011100000000011010001101110 / 1111 0011110000000001101000110111 / 1111 0100000000000000000000000000 / 1111 0100001111111110010111001010 / 1111 0100011111111100101110010011 / 1111 0100110000000001101000110111 / 1111 0101000000000000000000000000 / 1111 0101001111111110010111001010 / 1111 0101100000000011010001101110 / 1111 0101110000000001101000110111 / 1111 0110000000000000000000000000 / 1111 0110001111111110010111001010 / 1111 0110011111111100101110010011 / 1111 0110110000000001101000110111 / 1111 0111000000000000000000000000 / 1111 0111001111111110010111001010 / 1111 0111100000000011010001101110 / 1111 0111110000000001101000110111 / 1111 1000000000000000000000000000 / 1111 1000001111111110010111001010 / 1111 1000011111111100101110010011 / 1111 1000110000000001101000110111 / 1111 1001000000000000000000000000 / 1111 1001001111111110010111001010 / 1111 1001100000000011010001101110 / 1111 1001110000000001101000110111 / 1111 1010000000000000000000000000 / 1111 1010001111111110010111001010 / 1111 1010011110111100101110010011 / 1111 1010110000000001101000110111 / 1111 1011000000000000000000000000 / 1111 1011001111111110010111001010 / 1111 1011100000000011010001101110 / 1111 1011110000000001101000110111 / 1111 1100000000000000000000000000 / 1111 1100001111111110010111001010 / 1111 1100011111111100101110010011 / 1111 1100110000000001101000110111 / 1111 1101000000000000000000000000 / 1111 1101001111111110010111001010 / 1111 1101100000000011010001101110 / 1111 1101110000000001101000110111 / 1111 1110000000000000000000000000 / 1111 1110001111111110010111001010 / 1111 1110011111111100101110010101 / 1111 1110110000000001101000110111 / 1111 1111000000000000000000000000 / 1111 1111001111111110010111001010 / 1111 1111100000000011010001101110 / 1111 1111110000000001101000110111	00000000 / 003FE5C9 / 007FCB92 / 00C01A36 / 01000000 / 013FE5C9 / 0180346D / 01C01A36 / 02000000 / 023FE5C9 / 027FCB92 / 02C01A36 / 03000000 / 033FE5C9 / 0380346D / 03C01A36 / 04000000 / 043FE5C9 / 047FCB92 / 04C01A36 / 05000000 / 053FE5C9 / 0580346D / 05C01A36 / 06000000 / 063FE5C9 / 067FCB92 / 06C01A36 / 07000000 / 073FE5C9 / 0780346D / 07C01A36 / 08000000 / 083FE5C9 / 087FCB92 / 08C01A36 / 09000000 / 093FE5C9 / 0980346D / 09C01A36 / 0A000000 / 0A3FE5C9 / 0A7FCB92 / 0AC01A36 / 0B000000 / 0B3FE5C9 / 0B80346D / 0BC01A36 / 0C000000 / 0C3FE5C9 / 0C7FCB92 / 0CC01A36 / 0D000000 / 0D3FE5C9 / 0D80346D / 0DC01A36 / 0E000000 / 0E3FE5C9 / 0E3FE5C9 / 0EC01A36 / 0F000000 / 0F3FE5C9 / 0F80346D / 0FC01A36 / 10000000 / 0FC01A36 / 0F80346D / 0F3FE5C9 / 0F000000 / 0EC01A36 / 0E7FCB92 / 0E3FE5C9 / 0E000000 / 0DC01A36 / 0D80346D / 0D3FE5C9 / 0D000000 / 0CC01A36 / 0C7FCB92 / 0C3FE5C9 / 0C000000 / 0BC01A36 / 0B80346D / 0B3FE5C9 / 0B000000 / 0AC01A36 / 0A7BCB92 / 0A3FE5C9 / 0A000000 / 09C01A36 / 0980346D / 093FE5C9 / 09000000 / 08C01A36 / 087FCB92 / 083FE5C9 / 08000000 / 07C01A36 / 0780346D / 073FE5C9 / 07000000 / 06C01A36 / 067FCB92 / 063FE5C9 / 06000000 / 05C01A36 / 0580346D / 053FE5C9 / 06000000 / 04C01A36 / 047FCB92 / 043FE5C9 / 04000000 / 03C01A36 / 0380346D / 033FE5C9 / 03000000 / 02C01A36 / 027FCB92 / 023FE5C9 / 02000000 / 01C01A36 / 0180346D / 013FE5C9 / 01000000 / 00C01A36 / 007FCB92 / 003FE5C9 / 00000000 / FFC01A37 / FF80346E / FF3FE5CA / FF000000 / FEC01A37 / FE7FCB93 / FE3FE5CA / FE000000 / FDC01A37 / FD80346E / FD3FE5CA / FD000000 / FCC01A37 / FC7FCB93 / FC3FE5CA / FC000000 / FBC01A37 / FB80346E / FB3FE5CA / FB000000 / FAC01A37 / FA7BCB93 / FA3FE5CA / FA000000 / F9C01A37 / F980346E / F93FE5CA / F9000000 / F8C01A37 / F87FCB93 / F83FE5CA / F8000000 / F7C01A37 / F780346E / F73FE5CA / F7000000 / F6C01A37 / F67FCB93 / F63FE5CA / F6000000 / F5C01A37 / F580346E / F53FE5CA / F6000000 / F4C01A37 / F47FCB93 / F43FE5CA / F4000000 / F3C01A37 / F380346E / F33FE5CA / F3000000 / F2C01A37 / F27FCB93 / F23FE5CA / F2000000 / F1C01A37 / F180346E / F13FE5CA / F1000000 / F0C01A37 / F07FCB93 / F03FE5CA / F0000000 / F03FE5CA / F07FCB93 / F0C01A37 / F1000000 / F13FE5CA / F180346E / F1C01A37 / F2000000 / F23FE5CA / F27FCB93 / F2C01A37 / F3000000 / F33FE5CA / F380346E / F3C01A37 / F4000000 / F43FE5CA / F47FCB93 / F4C01A37 / F5000000 / F53FE5CA / F580346E / F5C01A37 / F6000000 / F63FE5CA / F67FCB93 / F6C01A37 / F7000000 / F73FE5CA / F780346E / F7C01A37 / F8000000 / F83FE5CA / F87FCB93 / F8C01A37 / F9000000 / F93FE5CA / F980346E / F9C01A37 / FA000000 / FA3FE5CA / FA7FCB93 / FAC01A37 / FB000000 / FB3FE5CA / FB80346E / FBC01A37 / FC000000 / FC3FE5CA / FC7FCB93 / FCC01A37 / FD000000 / FD3FE5CA / FD80346E / FDC01A37 / FE000000 / FE3FE5CA / FE7FCB93 / FEC01A37 / FF000000 / FF3FE5CA / FF80346E / FFC01A37

LUT	Sine			Cosine
	Dec	Bin	Hex	Dec	Bin	Hex
0 / 1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34 / 35 / 36 / 37 / 38 / 39 / 40 / 41 / 42 / 43 / 44 / 45 / 46 / 47 / 48 / 49 / 50 / 51 / 52 / 53 / 54 / 55 / 56 / 57 / 58 / 59 / 60 / 61 / 62 / 63 / 64 / 65 / 66 / 67 / 68 / 69 / 70 / 71 / 72 / 73 / 74 / 75 / 76 / 77 / 78 / 79 / 80 / 81 / 82 / 83 / 84 / 85 / 86 / 87 / 88 / 89 / 90 / 91 / 92 / 93 / 94 / 95 / 96 / 97 / 98 / 99 / 100 / 101 / 102 / 103 / 104 / 105 / 106 / 107 / 108 / 109 / 110 / 111 / 112 / 113 / 114 / 115 / 116 / 117 / 118 / 119 / 120 / 121 / 122 / 123 / 124 / 125 / 126 / 127 / 128 / 129 / 130 / 131 / 132 / 133 / 134 / 135 / 136 / 137 / 138 / 139 / 140 / 141 / 142 / 143 / 144 / 145 / 146 / 147 / 148 / 149 / 150 / 151 / 152 / 153 / 154 / 155 / 156 / 157 / 158 / 159 / 160 / 161 / 162 / 163 / 164 / 165 / 166 / 167 / 168 / 169 / 170 / 171 / 172 / 173 / 174 / 175 / 176 / 177 / 178 / 179 / 180 / 181 / 182 / 183 / 184 / 185 / 186 / 187 / 188 / 189 / 190 / 191 / 192 / 193 / 194 / 195 / 196 / 197 / 198 / 199 / 200 / 201 / 202 / 203 / 204 / 205 / 206 / 207 / 208 / 209 / 210 / 211 / 212 / 213 / 214 / 215 / 216 / 217 / 218 / 219 / 220 / 221 / 222 / 223 / 224 / 225 / 226 / 227 / 228 / 229 / 230 / 231 / 232 / 233 / 234 / 235 / 236 / 237 / 238 / 239 / 240 / 241 / 242 / 243 / 244 / 245 / 246 / 247 / 248 / 249 / 250 / 251 / 252 / 253 / 254 / 255	0.0000 / 0.0245 / 0.0491 / 0.0736 / 0.0980 / 0.1224 / 0.1467 / 0.1710 / 0.1951 / 0.2191 / 0.2430 / 0.2667 / 0.2903 / 0.3137 / 0.3369 / 0.3599 / 0.3827 / 0.4052 / 0.4276 / 0.4496 / 0.4714 / 0.4929 / 0.5141 / 0.5350 / 0.5556 / 0.5758 / 0.5957 / 0.6152 / 0.6344 / 0.6532 / 0.6716 / 0.6895 / 0.7071 / 0.7242 / 0.7410 / 0.7572 / 0.7730 / 0.7883 / 0.8032 / 0.8176 / 0.8315 / 0.8449 / 0.8577 / 0.8701 / 0.8819 / 0.8932 / 0.9040 / 0.9142 / 0.9239 / 0.9330 / 0.9415 / 0.9495 / 0.9569 / 0.9638 / 0.9700 / 0.9757 / 0.9808 / 0.9853 / 0.9892 / 0.9925 / 0.9952 / 0.9973 / 0.9988 / 0.9997 / 1.0000 / 0.9997 / 0.9988 / 0.9973 / 0.9952 / 0.9925 / 0.9892 / 0.9853 / 0.9808 / 0.9757 / 0.9700 / 0.9638 / 0.9569 / 0.9495 / 0.9415 / 0.9330 / 0.9239 / 0.9142 / 0.9040 / 0.8932 / 0.8819 / 0.8701 / 0.8577 / 0.8449 / 0.8315 / 0.8176 / 0.8032 / 0.7883 / 0.7730 / 0.7572 / 0.7410 / 0.7242 / 0.7071 / 0.6895 / 0.6716 / 0.6532 / 0.6344 / 0.6152 / 0.5957 / 0.5758 / 0.5556 / 0.5350 / 0.5141 / 0.4929 / 0.4714 / 0.4496 / 0.4276 / 0.4052 / 0.3827 / 0.3599 / 0.3369 / 0.3137 / 0.2903 / 0.2667 / 0.2430 / 0.2191 / 0.1951 / 0.1710 / 0.1467 / 0.1224 / 0.0980 / 0.0736 / 0.0491 / 0.0245 / 0.0000 / -0.0245 / -0.0491 / -0.0736 / -0.0980 / -0.1224 / -0.1467 / -0.1710 / -0.1951 / -0.2191 / -0.2430 / -0.2667 / -0.2903 / -0.3137 / -0.3369 / -0.3599 / -0.3827 / -0.4052 / -0.4276 / -0.4496 / -0.4714 / -0.4929 / -0.5141 / -0.5350 / -0.5556 / -0.5758 / -0.5957 / -0.6152 / -0.6344 / -0.6532 / -0.6716 / -0.6895 / -0.7071 / -0.7242 / -0.7410 / -0.7572 / -0.7730 / -0.7883 / -0.8032 / -0.8176 / -0.8315 / -0.8449 / -0.8577 / -0.8701 / -0.8819 / -0.8932 / -0.9040 / -0.9142 / -0.9239 / -0.9330 / -0.9415 / -0.9495 / -0.9569 / -0.9638 / -0.9700 / -0.9757 / -0.9808 / -0.9853 / -0.9892 / -0.9925 / -0.9952 / -0.9973 / -0.9988 / -0.9997 / -1.0000 / -0.9997 / -0.9988 / -0.9973 / -0.9952 / -0.9925 / -0.9892 / -0.9853 / -0.9808 / -0.9757 / -0.9700 / -0.9638 / -0.9569 / -0.9495 / -0.9415 / -0.9330 / -0.9239 / -0.9142 / -0.9040 / -0.8932 / -0.8819 / -0.8701 / -0.8577 / -0.8449 / -0.8315 / -0.8176 / -0.8032 / -0.7883 / -0.7730 / -0.7572 / -0.7410 / -0.7242 / -0.7071 / -0.6895 / -0.6716 / -0.6532 / -0.6344 / -0.6152 / -0.5957 / -0.5758 / -0.5556 / -0.5350 / -0.5141 / -0.4929 / -0.4714 / -0.4496 / -0.4276 / -0.4052 / -0.3827 / -0.3599 / -0.3369 / -0.3137 / -0.2903 / -0.2667 / -0.2430 / -0.2191 / -0.1951 / -0.1710 / -0.1467 / -0.1224 / -0.0980 / -0.0736 / -0.0491 / -0.0245	0000 0000000000000000000000000000 / 0000 0000011001000101101000011100 / 0000 0000110010010001110100010100 / 0000 0001001011010111011100110001 / 0000 0001100100010110100001110010 / 0000 0001111101010101100110110011 / 0000 0010010110001110001000011001 / 0000 0010101111000110101001111110 / 0000 0011000111110010000100101101 / 0000 0011100000010110111100000000 / 0000 0011111000110101001111110111 / 0000 0100010001000110011100111000 / 0000 0100101001010001000110011100 / 0000 0101000001001110101001001010 / 0000 0101011000111111000101000001 / 0000 0101110000100010011010000000 / 0000 0110000111111000101000001001 / 0000 0110011110111011001011111110 / 0000 0110110101110111001100011000 / 0000 0111001100011000111111000101 / 0000 0111100010101101101010111001 / 0000 0111111000101110101100011100 / 0000 1000001110011100000011101011 / 0000 1000100011110101110000101000 / 0000 1000111000111011110011010011 / 0000 1001001101100111101000001111 / 0000 1001100001111111110010111001 / 0000 1001110101111101101111110100 / 0000 1010001001101000000010011101 / 0000 1010011100111000000111010111 / 0000 1010101111101101111110100100 / 0000 1011000010000011000100100110 / 0000 1011010100000100100000010110 / 0000 1011100101100101001010111101 / 0000 1011110110110010001011010000 / 0000 1100000111010111110110111111 / 0000 1100010111100011010100111111 / 0000 1100100111001110000001110101 / 0000 1100110110011110100000111110 / 0000 1101000101001110001110111100 / 0000 1101010011011101001011110001 / 0000 1101100001001011010111011100 / 0000 1101101110010010001110100010 / 0000 1101111010111110110111111010 / 0000 1110000111000100001100101100 / 0000 1110010010101000110000010101 / 0000 1110011101101100100010110100 / 0000 1110101000001001000000101101 / 0000 1110110010000100101101011101 / 0000 1110111011011001000101101000 / 0000 1111000100000110001001001101 / 0000 1111001100010010011011101001 / 0000 1111010011110111011001011111 / 0000 1111011010111011100110001100 / 0000 1111100001010001111010111000 / 0000 1111100111000111011110011010 / 0000 1111101100010101101101010111 / 0000 1111110000111100100111101110 / 0000 1111110100111100001101100001 / 0000 1111111000010100011110101110 / 0000 1111111011000101011011010101 / 0000 1111111101001111000011011000 / 0000 1111111110110001010110110101 / 0000 1111111111101100010101101101 / 0001 0000000000000000000000000000 / 0000 1111111111101100010101101101 / 0000 1111111110110001010110110101 / 0000 1111111101001111000011011000 / 0000 1111111011000101011011010101 / 0000 1111111000010100011110101110 / 0000 1111110100111100001101100001 / 0000 1111110000111100100111101110 / 0000 1111101100010101101101010111 / 0000 1111100111000111011110011010 / 0000 1111100001010001111010111000 / 0000 1111011010111011100110001100 / 0000 1111010011110111011001011111 / 0000 1111001100010010011011101001 / 0000 1111000100000110001001001101 / 0000 1110111011011001000101101000 / 0000 1110110010000100101101011101 / 0000 1110101000001001000000101101 / 0000 1110011101101100100010110100 / 0000 1110010010101000110000010101 / 0000 1110000111000100001100101100 / 0000 1101111010111110110111111010 / 0000 1101101110010010001110100010 / 0000 1101100001001011010111011100 / 0000 1101010011011101001011110001 / 0000 1101000101001110001110111100 / 0000 1100110110011110100000111110 / 0000 1100100111001110000001110101 / 0000 1100010111100011010100111111 / 0000 1100000111010111110110111111 / 0000 1011110110110010001011010000 / 0000 1011100101100101001010111101 / 0000 1011010100000100100000010110 / 0000 1011000010000011000100100110 / 0000 1010101111101101111110100100 / 0000 1010011100111000000111010111 / 0000 1010001001101000000010011101 / 0000 1001110101111101101111110100 / 0000 1001100001111111110010111001 / 0000 1001001101100111101000001111 / 0000 1000111000111011110011010011 / 0000 1000100011110101110000101000 / 0000 1000001110011100000011101011 / 0000 0111111000101110101100011100 / 0000 0111100010101101101010111001 / 0000 0111001100011000111111000101 / 0000 0110110101110111001100011000 / 0000 0110011110111011001011111110 / 0000 0110000111111000101000001001 / 0000 0101110000100010011010000000 / 0000 0101011000111111000101000001 / 0000 0101000001001110101001001010 / 0000 0100101001010001000110011100 / 0000 0100010001000110011100111000 / 0000 0011111000110101001111110111 / 0000 0011100000010110111100000000 / 0000 0011000111110010000100101101 / 0000 0010101111000110101001111110 / 0000 0010010110001110001000011001 / 0000 0001111101010101100110110011 / 0000 0001100100010110100001110010 / 0000 0001001011010111011100110001 / 0000 0000110010010001110100010100 / 0000 0000011001000101101000011100 / 0000 0000000000000000000000000000 / 1111 1111100110111010010111100100 / 1111 1111001101101110001011101100 / 1111 1110110100101000100011001111 / 1111 1110011011101001011110001110 / 1111 1110000010101010011001001101 / 1111 1101101001110001110111100111 / 1111 1101010000111001010110000010 / 1111 1100111000001101111011010011 / 1111 1100011111101001000111111111 / 1111 1100000111001010110000001001 / 1111 1011101110111001100011001000 / 1111 1011010110101110111001100100 / 1111 1010111110110001010110110110 / 1111 1010100111000000111010111111 / 1111 1010001111011101100110000000 / 1111 1001111000000111010111110111 / 1111 1001100001000100110100000010 / 1111 1001001010001000110011101000 / 1111 1000110011100111000000111011 / 1111 1000011101010010010101000111 / 1111 1000000111010001010011100100 / 1111 0111110001100011111100010101 / 1111 0111011100001010001111011000 / 1111 0111000111000100001100101101 / 1111 0110110010011000010111110001 / 1111 0110011110000000001101000111 / 1111 0110001010000010010000001100 / 1111 0101110110010111111101100011 / 1111 0101100011000111111000101001 / 1111 0101010000010010000001011100 / 1111 0100111101111100111011011010 / 1111 0100101011111011011111101010 / 1111 0100011010011010110101000011 / 1111 0100001001001101110100110000 / 1111 0011111000101000001001000001 / 1111 0011101000011100101011000001 / 1111 0011011000110001111110001011 / 1111 0011001001100001011111000010 / 1111 0010111010110001110001000100 / 1111 0010101100100010110100001111 / 1111 0010011110110100101000100100 / 1111 0010010001101101110001011110 / 1111 0010000101000001001000000110 / 1111 0001111000111011110011010100 / 1111 0001101101010111001111101011 / 1111 0001100010010011011101001100 / 1111 0001010111110110111111010011 / 1111 0001001101111011010010100011 / 1111 0001000100100110111010011000 / 1111 0000111011111001110110110011 / 1111 0000110011101101100100010111 / 1111 0000101100001000100110100001 / 1111 0000100101000100011001110100 / 1111 0000011110101110000101001000 / 1111 0000011000111000100001100110 / 1111 0000010011101010010010101001 / 1111 0000001111000011011000010010 / 1111 0000001011000011110010011111 / 1111 0000000111101011100001010010 / 1111 0000000100111010100100101011 / 1111 0000000010110000111100101000 / 1111 0000000001001110101001001011 / 1111 0000000000010011101010010011 / 1111 0000000000000000000000000000 / 1111 0000000000010011101010010011 / 1111 0000000001001110101001001011 / 11110000000010110000111100101000 / 1111 0000000100111010100100101011 / 1111 0000000111101011100001010010 / 1111 0000001011000011110010011111 / 1111 0000001111000011011000010010 / 1111 0000010011101010010010101001 / 1111 0000011000111000100001100110 / 1111 0000011110101110000101001000 / 1111 0000100101000100011001110100 / 1111 0000101100001000100110100001 / 1111 0000110011101101100100010111 / 1111 0000111011111001110110110011 / 1111 0001000100100110111010011000 / 1111 0001001101111011010010100011 / 1111 0001010111110110111111010011 / 1111 0001100010010011011101001100 / 1111 0001101101010111001111101011 / 1111 0001111000111011110011010100 / 1111 0010000101000001001000000110 / 1111 0010010001101101110001011110 / 1111 0010011110110100101000100100 / 1111 0010101100100010110100001111 / 1111 0010111010110001110001000100 / 1111 0011001001100001011111000010 / 1111 0011011000110001111110001011 / 1111 0011101000011100101011000001 / 1111 0011111000101000001001000001 / 1111 0100001001001101110100110000 / 1111 0100011010011010110101000011 / 1111 0100101011111011011111101010 / 1111 0100111101111100111011011010 / 1111 0101010000010010000001011100 / 1111 0101100011000111111000101001 / 1111 0101110110010111111101100011 / 1111 0110001010000010010000001100 / 1111 0110011110000000001101000111 / 1111 0110110010011000010111110001 / 1111 0111000111000100001100101101 / 1111 0111011100001010001111011000 / 1111 0111110001100011111100010101 / 1111 1000000111010001010011100100 / 1111 1000011101010010010101000111 / 1111 1000110011100111000000111011 / 1111 1001001010001000110011101000 / 1111 1001100001000100110100000010 / 1111 1001111000000111010111110111 / 1111 1010001111011101100110000000 / 1111 1010100111000000111010111111 / 1111 1010111110110001010110110110 / 1111 1011010110101110111001100100 / 1111 1011101110111001100011001000 / 1111 1100000111001010110000001001 / 1111 1100011111101001000111111111 / 1111 1100111000001101111011010011 / 11111101010000111001010110000010 / 1111 1101101001110001110111100111 / 1111 1110000010101010011001001101 / 1111 1110011011101001011110001110 / 1111 1110110100101000100011001111 / 1111 1111001101101110001011101100 / 1111 1111100110111010010111100100	00000000 / 00645A1C / 00C91D14 / 012D7731 / 01916872 / 01F559B3 / 0258E219 / 02BC6A7E / 031F212D / 03816F00 / 03E353F7 / 04446738 / 04A5119C / 0504EA4A / 0563F141 / 05C22680 / 061F8A09 / 067BB2FE / 06D77318 / 07318FC5 / 078ADAB9 / 07E2EB1C / 0839C0EB / 088F5C28 / 08E3BCD3 / 09367A0F / 0987FCB9 / 09D7DBF4 / 0A26809D / 0A7381D7 / 0ABEDFA4 / 0B083126 / 0B504816 / 0B9652BD / 0BDB22D0 / 0C1D7DBF / 0C5E353F / 0C9CE075 / 0CD9E83E / 0D14E3BC / 0D4DD2F1 / 0D84B5DC / 0DB923A2 / 0DEBEDFA / 0E1C432C / 0E4A8C15 / 0E76C8B4 / 0EA0902D / 0EC84B5D / 0EED9168 / 0F10624D / 0F3126E9 / 0F4F765F / 0F6BB98C / 0F851EB8 / 0F9C779A / 0FB15B57 / 0FC3C9EE / 0FD3C361 / 0FE147AE / 0FEC56D5 / 0FF4F0D8 / 0FFB15B5 / 0FFEC56D / 10000000 / 0FFEC56D / 0FFB15B5 / 0FF4F0D8 / 0FEC56D5 / 0FE147AE / 0FD3C361 / 0FC3C9EE / 0FB15B57 / 0F9C779A / 0F851EB8 / 0F6BB98C / 0F4F765F / 0F3126E9 / 0F10624D / 0EED9168 / 0EC84B5D / 0EA0902D / 0E76C8B4 / 0E4A8C15 / 0E1C432C / 0DEBEDFA / 0DB923A2 / 0D84B5DC / 0D4DD2F1 / 0D14E3BC / 0CD9E83E / 0C9CE075 / 0C5E353F / 0C1D7DBF / 0BDB22D0 / 0B9652BD / 0B504816 / 0B083126 / 0ABEDFA4 / 0A7381D7 / 0A26809D / 09D7DBF4 / 0987FCB9 / 09367A0F / 08E3BCD3 / 088F5C28 / 0839C0EB / 07E2EB1C / 078ADAB9 / 07318FC5 / 06D77318 / 067BB2FE / 061F8A09 / 05C22680 / 0563F141 / 0504EA4A / 04A5119C / 04446738 / 03E353F7 / 03816F00 / 031F212D / 02BC6A7E / 0258E219 / 01F559B3 / 01916872 / 012D7731 / 00C91D14 / 00645A1C / 00000000 / FF9BA5E4 / FF36E2EC / FED288CF / FE6E978E / FE0AA64D / FDA71DE7 / FD439582 / FCE0DED3 / FC7E91FF / FC1CAC09 / FBBB98C8 / FB5AEE64 / FAFB15B6 / FA9C0EBF / FA3DD980 / F9E075F7 / F9844D02 / F9288CE8 / F8CE703B / F8752547 / F81D14E4 / F7C63F15 / F770A3D8 / F71C432D / F6C985F1 / F6780347 / F628240C / F5D97F63 / F58C7E29 / F541205C / F4F7CEDA / F4AFB7EA / F469AD43 / F424DD30 / F3E28241 / F3A1CAC1 / F3631F8B / F32617C2 / F2EB1C44 / F2B22D0F / F27B4A24 / F246DC5E / F2141206 / F1E3BCD4 / F1B573EB / F189374C / F15F6FD3 / F137B4A3 / F1126E98 / F0EF9DB3 / F0CED917 / F0B089A1 / F0944674 / F07AE148 / F0638866 / F04EA4A9 / F03C3612 / F02C3C9F / F01EB852 / F013A92B / F00B0F28 / F004EA4B / F0013A93 / F0000000 / F0013A93 / F004EA4B / F00B0F28 / F013A92B / F01EB852 / F02C3C9F / F03C3612 / F04EA4A9 / F0638866 / F07AE148 / F0944674 / F0B089A1 / F0CED917 / F0EF9DB3 / F1126E98 / F137B4A3 / F15F6FD3 / F189374C / F1B573EB / F1E3BCD4 / F2141206 / F246DC5E / F27B4A24 / F2B22D0F / F2EB1C44 / F32617C2 / F3631F8B / F3A1CAC1 / F3E28241 / F424DD30 / F469AD43 / F4AFB7EA / F4F7CEDA / F541205C / F58C7E29 / F5D97F63 / F628240C / F6780347 / F6C985F1 / F71C432D / F770A3D8 / F7C63F15 / F81D14E4 / F8752547 / F8CE703B / F9288CE8 / F9844D02 / F9E075F7 / FA3DD980 / FA9C0EBF / FAFB15B6 / FB5AEE64 / FBBB98C8 / FC1CAC09 / FC7E91FF / FCE0DED3 / FD439582 / FDA71DE7 / FE0AA64D / FE6E978E / FED288CF / FF36E2EC / FF9BA5E4	1.0000 / 0.9997 / 0.9988 / 0.9973 / 0.9952 / 0.9925 / 0.9892 / 0.9853 / 0.9808 / 0.9757 / 0.9700 / 0.9638 / 0.9569 / 0.9495 / 0.9415 / 0.9330 / 0.9239 / 0.9142 / 0.9040 / 0.8932 / 0.8819 / 0.8701 / 0.8577 / 0.8449 / 0.8315 / 0.8176 / 0.8032 / 0.7883 / 0.7730 / 0.7572 / 0.7410 / 0.7242 / 0.7071 / 0.6895 / 0.6716 / 0.6532 / 0.6344 / 0.6152 / 0.5957 / 0.5758 / 0.5556 / 0.5350 / 0.5141 / 0.4929 / 0.4714 / 0.4496 / 0.4276 / 0.4052 / 0.3827 / 0.3599 / 0.3369 / 0.3137 / 0.2903 / 0.2667 / 0.2430 / 0.2191 / 0.1951 / 0.1710 / 0.1467 0.1224 / 0.0980 / 0.0736 / 0.0491 / 0.0245 / 0.0000 / -0.0245 / -0.0491 / -0.0736 / -0.0980 / -0.1224 / -0.1467 / -0.1710 / -0.1951 / -0.2191 / -0.2430 / -0.2667 / -0.2903 / -0.3137 / -0.3369 / -0.3599 / -0.3827 / -0.4052 / -0.4276 / -0.4496 / -0.4714 / -0.4929 / -0.5141 / -0.5350 / -0.5556 / -0.5758 / -0.5957 / -0.6152 / -0.6344 / -0.6532 / -0.6716 / -0.6895 / -0.7071 / -0.7242 / -0.7410 / -0.7572 / -0.7730 / -0.7883 / -0.8032 / -0.8176 / -0.8315 / -0.8449 / -0.8577 / -0.8701 / -0.8819 / -0.8932 / -0.9040 / -0.9142 / -0.9239 / -0.9330 / -0.9415 / -0.9495 / -0.9569 / -0.9638 / -0.9700 / -0.9757 / -0.9808 / -0.9853 / -0.9892 / -0.9925 / -0.9952 / -0.9973 / -0.9988 / -0.9997 / -1.0000 / -0.9997 / -0.9988 / -0.9973 / -0.9952 / -0.9925 / -0.9892 / -0.9853 / -0.9808 / -0.9757 / -0.9700 / -0.9638 / -0.9569 / -0.9495 / -0.9415 / -0.9330 / -0.9239 / -0.9142 / -0.9040 / -0.8932 / -0.8819 / -0.8701 / -0.8577 / -0.8449 / -0.8315 / -0.8176 / -0.8032 / -0.7883 / -0.7730 / -0.7572 / -0.7410 / -0.7242 / -0.7071 / -0.6895 / -0.6716 / -0.6532 / -0.6344 / -0.6152 / -0.5957 / -0.5758 / -0.5556 / -0.5350 / -0.5141 / -0.4929 / -0.4714 / -0.4496 / -0.4276 / -0.4052 / -0.3827 / -0.3599 / -0.3369 / -0.3137 / -0.2903 / -0.2667 / -0.2430 / -0.2191 / -0.1951 / -0.1710 / -0.1467 / -0.1224 / -0.0980 / -0.0736 / -0.0491 / -0.0245 / 0.0000 / 0.0245 / 0.0491 / 0.0736 / 0.0980 / 0.1224 / 0.1467 / 0.1710 / 0.1951 / 0.2191 / 0.2430 / 0.2667 / 0.2903 / 0.3137 / 0.3369 / 0.3599 / 0.3827 / 0.4052 / 0.4276 / 0.4496 / 0.4714 / 0.4929 / 0.5141 / 0.5350 / 0.5556 / 0.5758 / 0.5957 / 0.6152 / 0.6344 / 0.6532 / 0.6716 / 0.6895 / 0.7071 / 0.7242 / 0.7410 / 0.7572 / 0.7730 / 0.7883 / 0.8032 / 0.8176 / 0.8315 / 0.8449 / 0.8577 / 0.8701 / 0.8819 / 0.8932 / 0.9040 / 0.9142 / 0.9239 / 0.9330 / 0.9415 / 0.9495 / 0.9569 / 0.9638 / 0.9700 / 0.9757 / 0.9808 / 0.9853 / 0.9892 / 0.9925 / 0.9952 / 0.9973 / 0.9988 / 0.9997	0001 0000000000000000000000000000 / 0000 1111111111101100010101101101 / 0000 1111111110110001010110110101 / 0000 1111111101001111000011011000 / 0000 1111111011000101011011010101 / 0000 1111111000010100011110101110 / 0000 1111110100111100001101100001 / 0000 1111110000111100100111101110 / 0000 1111101100010101101101010111 / 0000 1111100111000111011110011010 / 0000 1111100001010001111010111000 / 0000 1111011010111011100110001100 / 0000 1111010011110111011001011111 / 0000 1111001100010010011011101001 / 0000 1111000100000110001001001101 / 0000 1110111011011001000101101000 / 0000 1110110010000100101101011101 / 0000 1110101000001001000000101101 / 0000 1110011101101100100010110100 / 0000 1110010010101000110000010101 / 0000 1110000111000100001100101100 / 0000 1101111010111110110111111010 / 0000 1101101110010010001110100010 / 0000 1101100001001011010111011100 / 0000 1101010011011101001011110001 / 0000 1101000101001110001110111100 / 0000 1100110110011110100000111110 / 0000 1100100111001110000001110101 / 0000 1100010111100011010100111111 / 0000 1100000111010111110110111111 / 0000 1011110110110010001011010000 / 0000 1011100101100101001010111101 / 0000 1011010100000100100000010110 / 0000 1011000010000011000100100110 / 0000 1010101111101101111110100100 / 0000 1010011100111000000111010111 / 0000 1010001001101000000010011101 / 0000 1001110101111101101111110100 / 0000 1001100001111111110010111001 / 0000 1001001101100111101000001111 / 0000 1000111000111011110011010011 / 0000 1000100011110101110000101000 / 0000 1000001110011100000011101011 / 0000 0111111000101110101100011100 / 0000 0111100010101101101010111001 / 0000 0111001100011000111111000101 / 0000 0110110101110111001100011000 / 0000 0110011110111011001011111110 / 0000 0110000111111000101000001001 / 0000 0101110000100010011010000000 / 0000 0101011000111111000101000001 / 0000 0101000001001110101001001010 / 0000 0100101001010001000110011100 / 0000 0100010001000110011100111000 / 0000 0011111000110101001111110111 / 0000 0011100000010110111100000000 / 0000 0011000111110010000100101101 / 0000 0010101111000110101001111110 / 0000 0010010110001110001000011001 / 0000 0001111101010101100110110011 / 0000 0001100100010110100001110010 / 0000 0001001011010111011100110001 / 0000 0000110010010001110100010100 / 0000 0000011001000101101000011100 / 0000 0000000000000000000000000000 / 1111 1111100110111010010111100100 / 1111 1111001101101110001011101100 / 1111 1110110100101000100011001111 / 1111 1110011011101001011110001110 / 1111 1110000010101010011001001101 / 1111 1101101001110001110111100111 / 11111101010000111001010110000010 / 1111 1100111000001101111011010011 / 1111 1100011111101001000111111111 / 1111 1100000111001010110000001001 / 1111 1011101110111001100011001000 / 1111 1011010110101110111001100100 / 1111 1010111110110001010110110110 / 1111 1010100111000000111010111111 / 1111 1010001111011101100110000000 / 1111 1001111000000111010111110111 / 1111 1001100001000100110100000010 / 11111001001010001000110011101000 / 1111 1000110011100111000000111011 / 1111 1000011101010010010101000111 / 1111 1000000111010001010011100100 / 1111 0111110001100011111100010101 / 1111 0111011100001010001111011000 / 1111 0111000111000100001100101101 / 1111 0110110010011000010111110001 / 1111 0110011110000000001101000111 / 1111 0110001010000010010000001100 / 1111 0101110110010111111101100011 / 1111 0101100011000111111000101001 / 1111 0101010000010010000001011100 / 1111 0100111101111100111011011010 / 1111 0100101011111011011111101010 / 1111 0100011010011010110101000011 / 1111 0100001001001101110100110000 / 1111 0011111000101000001001000001 / 1111 0011101000011100101011000001 / 1111 0011011000110001111110001011 / 1111 0011001001100001011111000010 / 1111 0010111010110001110001000100 / 1111 0010101100100010110100001111 / 11110010011110110100101000100100 / 1111 0010010001101101110001011110 / 1111 0010000101000001001000000110 / 1111 0001111000111011110011010100 / 1111 0001101101010111001111101011 / 1111 0001100010010011011101001100 / 1111 0001010111110110111111010011 / 1111 0001001101111011010010100011 / 1111 0001000100100110111010011000 / 1111 0000111011111001110110110011 / 1111 0000110011101101100100010111 / 1111 0000101100001000100110100001 / 1111 0000100101000100011001110100 / 1111 0000011110101110000101001000 / 1111 0000011000111000100001100110 / 1111 0000010011101010010010101001 / 1111 0000001111000011011000010010 / 1111 0000001011000011110010011111 / 1111 0000000111101011100001010010 / 1111 0000000100111010100100101011 / 11110000000010110000111100101000 / 1111 0000000001001110101001001011 / 1111 0000000000010011101010010011 / 1111 0000000000000000000000000000 / 1111 0000000000010011101010010011 / 1111 0000000001001110101001001011 / 11110000000010110000111100101000 / 1111 0000000100111010100100101011 / 1111 0000000111101011100001010010 / 1111 0000001011000011110010011111 / 1111 0000001111000011011000010010 / 1111 0000010011101010010010101001 / 1111 0000011000111000100001100110 / 1111 0000011110101110000101001000 / 1111 0000100101000100011001110100 / 1111 0000101100001000100110100001 / 1111 0000110011101101100100010111 / 1111 0000111011111001110110110011 / 1111 0001000100100110111010011000 / 1111 0001001101111011010010100011 / 1111 0001010111110110111111010011 / 1111 0001100010010011011101001100 / 1111 0001101101010111001111101011 / 1111 0001111000111011110011010100 / 1111 0010000101000001001000000110 / 1111 0010010001101101110001011110 / 1111 0010011110110100101000100100 / 1111 0010101100100010110100001111 / 1111 0010111010110001110001000100 / 1111 0011001001100001011111000010 / 1111 0011011000110001111110001011 / 1111 0011101000011100101011000001 / 1111 0011111000101000001001000001 / 1111 0100001001001101110100110000 / 1111 0100011010011010110101000011 / 1111 0100101011111011011111101010 / 1111 0100111101111100111011011010 / 1111 0101010000010010000001011100 / 1111 0101100011000111111000101001 / 1111 0101110110010111111101100011 / 1111 0110001010000010010000001100 / 1111 0110011110000000001101000111 / 1111 0110110010011000010111110001 / 1111 0111000111000100001100101101 / 1111 0111011100001010001111011000 / 1111 0111110001100011111100010101 / 1111 1000000111010001010011100100 / 1111 1000011101010010010101000111 / 1111 1000110011100111000000111011 / 1111 1001001010001000110011101000 / 1111 1001100001000100110100000010 / 1111 1001111000000111010111110111 / 1111 1010001111011101100110000000 / 1111 1010100111000000111010111111 / 1111 1010111110110001010110110110 / 1111 1011010110101110111001100100 / 1111 1011101110111001100011001000 / 1111 1100000111001010110000001001 / 1111 1100011111101001000111111111 / 1111 1100111000001101111011010011 / 11111101010000111001010110000010 / 1111 1101101001110001110111100111 / 1111 1110000010101010011001001101 / 1111 1110011011101001011110001110 / 1111 1110110100101000100011001111 / 1111 1111001101101110001011101100 / 1111 1111100110111010010111100100 / 0000 0000000000000000000000000000 / 0000 0000011001000101101000011100 / 0000 0000110010010001110100010100 / 0000 0001001011010111011100110001 / 0000 0001100100010110100001110010 / 0000 0001111101010101100110110011 / 0000 0010010110001110001000011001 / 0000 0010101111000110101001111110 / 0000 0011000111110010000100101101 / 0000 0011100000010110111100000000 / 0000 0011111000110101001111110111 / 0000 0100010001000110011100111000 / 0000 0100101001010001000110011100 / 0000 0101000001001110101001001010 / 0000 0101011000111111000101000001 / 0000 0101110000100010011010000000 / 0000 0110000111111000101000001001 / 0000 0110011110111011001011111110 / 0000 0110110101110111001100011000 / 0000 0111001100011000111111000101 / 0000 0111100010101101101010111001 / 0000 0111111000101110101100011100 / 0000 1000001110011100000011101011 / 0000 1000100011110101110000101000 / 0000 1000111000111011110011010011 / 0000 1001001101100111101000001111 / 0000 1001100001111111110010111001 / 0000 1001110101111101101111110100 / 0000 1010001001101000000010011101 / 0000 1010011100111000000111010111 / 0000 1010101111101101111110100100 / 0000 1011000010000011000100100110 / 0000 1011010100000100100000010110 / 0000 1011100101100101001010111101 / 0000 1011110110110010001011010000 / 0000 1100000111010111110110111111 / 0000 1100010111100011010100111111 / 0000 1100100111001110000001110101 / 0000 1100110110011110100000111110 / 0000 1101000101001110001110111100 / 0000 1101010011011101001011110001 / 0000 1101100001001011010111011100 / 0000 1101101110010010001110100010 / 0000 1101111010111110110111111010 / 0000 1110000111000100001100101100 / 0000 1110010010101000110000010101 / 0000 1110011101101100100010110100 / 0000 1110101000001001000000101101 / 0000 1110110010000100101101011101 / 0000 1110111011011001000101101000 / 0000 1111000100000110001001001101 / 0000 1111001100010010011011101001 / 0000 1111010011110111011001011111 / 0000 1111011010111011100110001100 / 0000 1111100001010001111010111000 / 0000 1111100111000111011110011010 / 0000 1111101100010101101101010111 / 0000 1111110000111100100111101110 / 0000 1111110100111100001101100001 / 0000 1111111000010100011110101110 / 0000 1111111011000101011011010101 / 0000 1111111101001111000011011000 / 0000 1111111110110001010110110101 / 0000 1111111111101100010101101101	10000000 / 0FFEC56D / 0FFB15B5 / 0FF4F0D8 / 0FEC56D5 / 0FE147AE / 0FD3C361 / 0FC3C9EE / 0FB15B57 / 0F9C779A / 0F851EB8 / 0F6BB98C / 0F4F765F / 0F3126E9 / 0F10624D / 0EED9168 / 0EC84B5D / 0EA0902D / 0E76C8B4 / 0E4A8C15 / 0E1C432C / 0DEBEDFA / 0DB923A2 / 0D84B5DC / 0D4DD2F1 / 0D14E3BC / 0CD9E83E / 0C9CE075 / 0C5E353F / 0C1D7DBF / 0BDB22D0 / 0B9652BD / 0B504816 / 0B083126 / 0ABEDFA4 / 0A7381D7 / 0A26809D / 09D7DBF4 / 0987FCB9 / 09367A0F / 08E3BCD3 / 088F5C28 / 0839C0EB / 07E2EB1C / 078ADAB9 / 07318FC5 / 06D77318 / 067BB2FE / 061F8A09 / 05C22680 / 0563F141 / 0504EA4A / 04A5119C / 04446738 / 03E353F7 / 03816F00 / 031F212D / 02BC6A7E / 0258E219 / 01F559B3 / 01916872 / 012D7731 / 00C91D14 / 00645A1C / 00000000 / FF9BA5E4 / FF36E2EC / FED288CF / FE6E978E / FE0AA64D / FDA71DE7 / FD439582 / FCE0DED3 / FC7E91FF / FC1CAC09 / FBBB98C8 / FB5AEE64 / FAFB15B6 / FA9C0EBF / FA3DD980 / F9E075F7 / F9844D02 / F9288CE8 / F8CE703B / F8752547 / F81D14E4 / F7C63F15 / F770A3D8 / F71C432D / F6C985F1 / F6780347 / F628240C / F5D97F63 / F58C7E29 / F541205C / F4F7CEDA / F4AFB7EA / F469AD43 / F424DD30 / F3E28241 / F3A1CAC1 / F3631F8B / F32617C2 / F2EB1C44 / F2B22D0F / F27B4A24 / F246DC5E / F2141206 / F1E3BCD4 / F1B573EB / F189374C / F15F6FD3 / F137B4A3 / F1126E98 / F0EF9DB3 / F0CED917 / F0B089A1 / F0944674 / F07AE148 / F0638866 / F04EA4A9 / F03C3612 / F02C3C9F / F01EB852 / F013A92B / F00B0F28 / F004EA4B / F0013A93 / F0000000 / F0013A93 / F004EA4B / F00B0F28 / F013A92B / F01EB852 / F02C3C9F / F03C3612 / F04EA4A9 / F0638866 / F07AE148 / F0944674 / F0B089A1 / F0CED917 / F0EF9DB3 / F1126E98 / F137B4A3 / F15F6FD3 / F189374C / F1B573EB / F1E3BCD4 / F2141206 / F246DC5E / F27B4A24 / F2B22D0F / F2EB1C44 / F32617C2 / F3631F8B / F3A1CAC1 / F3E28241 / F424DD30 / F469AD43 / F4AFB7EA / F4F7CEDA / F541205C / F58C7E29 / F5D97F63 / F628240C / F6780347 / F6C985F1 / F71C432D / F770A3D8 / F7C63F15 / F81D14E4 / F8752547 / F8CE703B / F9288CE8 / F9844D02 / F9E075F7 / FA3DD980 / FA9C0EBF / FAFB15B6 / FB5AEE64 / FBBB98C8 / FC1CAC09 / FC7E91FF / FCE0DED3 / FD439582 / FDA71DE7 / FE0AA64D / FE6E978E / FED288CF / FF36E2EC / FF9BA5E4 / 00000000 / 00645A1C / 00C91D14 / 012D7731 / 01916872 / 01F559B3 / 0258E219 / 02BC6A7E / 031F212D / 03816F00 / 03E353F7 / 04446738 / 04A5119C / 0504EA4A / 0563F141 / 05C22680 / 061F8A09 / 067BB2FE / 06D77318 / 07318FC5 / 078ADAB9 / 07E2EB1C / 0839C0EB / 088F5C28 / 08E3BCD3 / 09367A0F / 0987FCB9 / 09D7DBF4 / 0A26809D / 0A7381D7 / 0ABEDFA4 / 0B083126 / 0B504816 / 0B9652BD / 0BDB22D0 / 0C1D7DBF / 0C5E353F / 0C9CE075 / 0CD9E83E / 0D14E3BC / 0D4DD2F1 / 0D84B5DC / 0DB923A2 / 0DEBEDFA / 0E1C432C / 0E4A8C15 / 0E76C8B4 / 0EA0902D / 0EC84B5D / 0EED9168 / 0F10624D / 0F3126E9 / 0F4F765F / 0F6BB98C / 0F851EB8 / 0F9C779A / 0FB15B57 / 0FC3C9EE / 0FD3C361 / 0FE147AE / 0FEC56D5 / 0FF4F0D8 / 0FFB15B5 / 0FFEC56D

## module code